## Slide 1
Wrench-a-Roni
Custom wrench design and testing
Michele Haugh
Lillian Letiecq
Mary Teifel
ENGR 1101 · Section 101
October 21, 2026

## Slide 2
Project Overview
Customer needs and design requirements
Engineering principles
Prototype 1 and revised Prototype 2
Comparison, evaluation, and future improvements

## Slide 3
Define the problem
Twinkle Toes Inc.
A toy company producing toddler playsets
Needs an inexpensive, functional, reusable wrench
Objective: a comfortable twisting tool that is easy to reproduce

## Slide 4
Generate concepts and requirements
Selected concept: three pieces with a two-handed twisting handle
Fit a standard ½-inch hex bolt head
Withstand at least 40 lb-in of torque
PLA printing with 0–50% infill allowed
Build plate: 203(W) × 232(H) × 203(L) mm
Both iterations use 20% triangular infill

## Slide 5
Develop a solution
Torque
τ = rF sin θ= r x F
Force and effective lever arm
Average compressive stress
σ = F / A
Load distributed over contact area
Production cost
C = 0.40m + 0.02t
m in oz, t in minutes, C in dollars
Notes: .

## Slide 6
Prototype 1: construction
Main wrench body
Tapered inner handle
Textured outer handle
3.0 oz, no supports
330-minute print

## Slide 7
Base Wrench Design 1

## Slide 8
Peg Wrench Design 1

## Slide 9
Handle Wrench Design 1

## Slide 10
Prototype 1: testing
40 lb-in
Requirement met
70 lb-in
Reported failure torque
Tight fit required excessive assembly force
The inner handle broke along a printed layer
Revision priorities: assembly fit, strength, and printing efficiency

## Slide 11
Prototype 2: design revisions
Revised body
Revised tapered inner handle
Body reduction in report: 1.0 to 0.6 in*
Cylinder fit reduction: 2%
Horizontal inner-handle print with supports
20% triangular infill retained

## Slide 12
Design 2 Base Blueprint

## Slide 13
Design 2 Peg Blueprint

## Slide 14
Prototype 2: testing
40 lb-in
Requirement met
80 lb-in
Hex opening deformed
2.5 oz including supports, 280-minute print
Some inner-handle material deformed during cooling
The prototype remained functional during the reported test

## Slide 15
Comparison of both designs
Measurement | Design 1 | Revised Design 2
Reported weight | 3.0 oz, no supports | 2.5 oz, with supports
Printing time | 330 min | 280 min
Filament cost | $1.20 | $1.00
Printing cost | $6.60 | $5.60
Total production cost | $7.80 | $6.60
40 lb-in requirement | Met | Met
Reported failure torque | 70 lb-in | 80 lb-in
Design 2: $1.20 lower cost and 50 minutes less printing

## Slide 16
Evaluate the solution
Revised Design 2 is the stronger project candidate
Meets the assigned 40 lb-in torque requirement
Lower reported cost
Shorter print time
Remaining limitations: opening deformation and inner-handle print quality

## Slide 17
Future improvements
Strengthen the hex opening against deformation
Remove about 0.5 in of excess outer-handle height
Explore fewer components and simpler assembly
Refine print orientation and settings, then retest
Notes: .

## Slide 18
Why Twinkle Toes Inc. Should Choose Wrench-a-Roni
Fun unique design kids enjoy better than traditional wrench
Ease of use for children
Practice motor skills and hand eye coordination for toddlers
Lightweight design

## Slide 19
Thank you
Questions?
Wrench-a-Roni
Michele Haugh, Lillian Letiecq, and Mary Teifel
Notes: Thank the audience and invite questions.